## Slide 1
Dr. Jim Graham and Chris Muhl
Humboldt State University, 2014

## Slide 2: The Need
Error varies greatly between projections and their settings
Computing error in projections can be time-consuming
Projections can be difficult for students to appreciate

## Slide 3
Projections greatly distort area, distance, and/or shape (form)
Mercator
0 to 50 area and distance distortion

## Slide 4
The nature of distortion can be difficult to describe in text
Oblique Mercator
0 to 10 area and distance distortion

## Slide 5
Clipping Bounds are required
Cassini
Soldner
Projection
Clipping bounds are also needed
Default
Limited to 0 to 2x distance distortion
Notes: Cassini Soldner, default settings

## Slide 6: Previously, to Compute Area Distortion
Create “Fishnet” of polygons
Project to equal-area projection
Compute “Exact” areas
Project to desired projection
Compute projected areas
Divide the exact by projected area values
  <1: area was made much smaller than expected
  >1: area was made larger than expected

## Slide 7: Today:
Selection projection
Enter desired settings
Press “Update”
“OK” to add layers

## Slide 9: Albers Equal Area Conic
Preserves Area and Form
Distorts Distance

## Slide 11: The Approach
BlueSpray
  Created by SchoonerTurtles, Inc.
  Provided free under a beta testing agreement
GDAL, GeoTools
  Open source projection engines
Also:
  Java from Oracle
  Java Topology Suite
  NetBeans

## Slide 12
Create grid of points along lines of latitude and longitude (parallels and meridians)

## Slide 13
Compute:
  Great circle area
  Great circle distances (along meridians and parallels)
  Angles are at intersections are 90 degrees except for the poles

## Slide 14
Project the grid of points to desired projection

## Slide 15
Compute area of “cells” between points
Divide by expected area
Compute the length of each line segment
Divide by expected length

## Slide 16
Compute the average change in angle at each point
  Sum the angle between all the line segments at each point
  Divide by the number of angles to find the average angle
  Divide by expected value of 90 dgrees

## Slide 17: Finding the bounds
Start at the center (0,0)
Moving left and right two cells then up and down one cell:
  Add cells that are within the specified tolerances
  Check for overlapping points
  Check for intersecting lines

## Slide 18: Adding “Cells”
Assumed the first four cells were within tolerances

## Slide 19: Adding “Cells”
Add cells to left and right that are within tolerance
3
4
1
2

## Slide 20: Adding “Cells”
Add additional cells to the left and right since the world is twice as wide as it is call (with Geographic data)
3
4
1
2
7
8
5
6

## Slide 21: Adding “Cells”
Add cells along the top and bottom.
Keep repeating the cycle until no more cells are added
3
4
1
2
12
9
13
10
15
18
19
16
7
8
14
20
5
6
11
17

## Slide 22: Disallow Intersections and Overlaps

## Slide 23: Limit Distortion
0 to 2x on area and distance

## Slide 24: Details
Accessing vector data from an applet
  Used BlueSprays “stx” format
Java Topology Suite is very picky
Projected Systems can extend beyond +-180 to +-90 degrees
  Used a 360*3, 180*3 sized grid for analysis

## Slide 25
Aitoff
Lambert
Conformal
Conic
Oblique
Stereographic
Lambert
Azimuthal
Equal Area

## Slide 26
Orthographic
Polar
Stereographic
Polyconic
Robinson

## Slide 27: Available At:
Applet:
  HSU Geospatial Web Site
  www.humboldt.edu/gsp -> Links
BlueSpray:
  SchoonerTurtles web site:
  www.schoonerturtles.com

## Slide 28: Future Steps
Add the ability to project from any layer
  Not just the globe
Finish projection engine within BlueSpray
  Uses the Projection Explorer to set the bounds

## Slide 29: Acknowledgments
Jake Nelson, Dr. Bernhard Jenny at Oregon State University
Nick Ramirez at Humboldt State University
Greg Newman at Colorado State University
All the folks that support open source GIS software: GDAL, GeoTools, Proj4, JTS, NetBeans, etc.